# Subsystem command reference
This section summarizes the Standard Commands for Programmable Instruments (SCPI) available to program the PSU over the remote interface.
- ABORt
- CALibrate
- DIAGnostic
- DISPlay
- FETCh
- INITiate
- INSTrument
- MEASure
- MEMory
- MMEMory
- OUTPut
- SENSe
- SOURce
- STATus
- SYSTem
- TRIGger
## ABORT
Abort commands cancel any triggered actions.

SCPI command	Description
ABORt	Resets the trigger system to the Idle state
:ELOG	Stops the data logging

### ABORt
Syntax	ABORt
Description	The ABORt command resets the trigger system and places all trigger sequences in the IDLE state. Any actions related to the trigger system that are in progress will be also aborted as quickly as possible. As a result, subsequent triggers have no effect on the input level. / ABORt is also executed at power-on and upon execution of the *RST command.
Usage example	ABOR
Related Commands	*RST / INITiate / [SOURce[<n>]]:CURRent:TRIGgered / [SOURce[<n>]]:VOLTage:TRIGgered / [SOURce[<n>]]:LIST:COUNt

### ABORt:ELOG
Syntax	ABORt:ELOG {<channel>}
Description	This command stops the data logging on the specified channel. / ABORt:ELOG is also executed at power-on and upon execution of the *RST command.
Parameters	Name	Type	Range	Default
	<channel>	Discrete	CH1|CH2	–
Usage example	ABOR:ELOG CH1
Related Commands	*RST