# Software simulator
The PSU firmware can be also compiled and executed as a Windows, Linux or OS X application. The software simulator is a terminal application that can respond to any currently supported SCPI command described in this document. SCPI commands could be entered directly in the simulator’s terminal window (Fig. 1) or remotely by using the e.g. a Telnet client (Fig. 2).

Fig. 1: Simulator welcome screen

Fig. 2: Remote connection using a telnet client
The simulator also has a GUI part when started open a separate window with the picture of the PSU front panel. The GUI depends of what revision is used that can be set in conf_user_revision.h file before simulator compilation.

Fig. 3: Simulator GUI for portrait front panel (r1B9)

Fig. 4: Simulator GUI for landscape front panel (r3B4)
The GUI simulator front panel currently displays only changes in LED indicators and indicates if load is applied on the output terminals or not. For example if 8.2 Ohm load is connected to the channel 2 and cause that channel enters CC mode the GUI front panel will indicate that in the following way:

Fig. 5: Simulator GUI with connected load on the channel 2
## SIMUlator
The SIMUlator subsystem represent a set of unclassified SCPI commands that can be used to manage external parameters and events such as load impedance, connection and disconnection of the load, sensor temperature or the PSU control circuit power supply state. Thanks to them e.g. simulation of the measuring and protection commands that depends of external events become more meaningful.
For example MEASure:CURRent? without connected load will always returns zero, or activation of the VOLTage:PROTection:STATe will automatically trip the OVP since channel cannot starts in CC mode of operation when output is switched on, etc.

SCPI command	Description
SIMUlator
:EXIT	Closes simulator
:GUI	Starts simulator’s GUI
:LOAD {<resistance>}	Sets value of the virtual load
:STATe {<bool>}	“Connects” virtual load to the channel output
:PIN1 {<bool>}	Sets value of the PIN1 input
:PWRGood {<bool>}	Sets the PWRGOOD signal state
:RPOL {<bool>}	Sets the RPOL signal state
:TEMP {<temperature>}	Sets the temperature sensor value
:VOLT:PROG:EXT {<voltage>}	Sets the output voltage when channel is in external programming mode

### SIMUlator:EXIT
Syntax	SIMUlator:EXIT
Description	This command close all Software simulators windows (terminal and GUI if started).
Return	None
Usage example	SIMU:EXIT

### SIMUlator:GUI
Syntax	SIMUlator:GUI
Description	Use this command to start the GUI simulator in the new window (see Fig. 3 and Fig. 4).
Return	None
Usage example	SIMU:GUI
Related Commands	SIMUlator:EXIT

### SIMUlator:LOAD
Syntax	SIMUlator:LOAD {<resistance>} / SIMUlator:LOAD?
Description	This command is used to define impedance of the virtual load that is connected to the channel output. Units are in ohms. With load connected it is possible to simulate e.g. CC mode of operation, current and power measurement, OCP and OPP functionality, etc. / Load value can be also changed by click and drag on the load’s image. Move cursor to the left to decrease, or to the right to increase value in increments of 1 Ω. / The simulator currently cannot emulate the “UR” mode of operation (see the OUTPut:MODE? command).
Parameters	Name	Type	Range	Default
	<resistance>	Numeric	0 – 9999999|INFinite	–
Return	The query command returns the programmed load value.
Usage example	SIMU:LOAD 8.2
Related Commands	OUTPut:MODE?

### SIMUlator:LOAD:STATe
Syntax	SIMUlator:LOAD:STATe {<bool>} / SIMUlator:LOAD:STATe?
Description	This command is used to “connect” or “disconnect” the virtual load to the channel output. If the GUI simulator is started (the SIMUlator:GUI command) load symbol with selected value in Ohms will be displayed (See Fig. 5). / Another possibility to connect (or disconnect) a load is by click on its image.
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	–
Return	The query command returns the load state.
Usage example	SIMU:LOAD:STAT? / 0 / MEAS:CURR? / 0.00 / SIMU:LOAD:STAT ON / MEAS:CURR? / 1.50
Related Commands	OUTPut:MODE? / SIMUlator:GUI / SIMUlator:LOAD

### SIMUlator:PIN1
Syntax	SIMUlator:PIN1 {<bool>} / SIMUlator:PIN1?
Description	This command can be used to simulate state on the PIN1 input on the PSU front panel push-in connector that can be used for initiate trigger.
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	–
Return	The query command returns the simulated PIN1 input state.
Usage example	VOLT:TRIG 12.00 / CURR:TRIG 2.50 / TRIG:SOUR PIN1 / OUTP 1 / INIT / SIMU:PIN1
Related Commands	ABORt / INITiate[:IMMediate] / TRIGger[:SEQuence]:DELay / TRIGger[:SEQuence]:SLOPe / TRIGger[:SEQuence]:SOURce

### SIMUlator:PWRGood
Syntax	SIMUlator:PWRGood {<bool>} / SIMUlator:PWRGood?
Description	This command can be used to simulate detection of an internal power supply failure. When PWRGOOD signal is changed from 1 to 0 the PSU is going to the Stand-by mode (equal to the command SYSTem:POW OFF). The PSU mode cannot be changed until PWRGOOD is not changed to 1.
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	ON
Return	The query command returns the PWRGOOD signal state.
Usage example	SYST:POW? / 1 / SIMU:PWRG 0 / SYST:POW? / 0
Related Commands	SYSTem:POWer

### SIMUlator:RPOL
Syntax	SIMUlator:RPOL {<bool>} / SIMUlator:RPOL?
Description	This command can be used to simulate detection of remote sensing reverse polarity condition.
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	ON
Return	The query command returns the RPOL signal state.
Usage example	STAT:QUES:INST:ISUM2? / 0 / SIMU:RPOL 1 / STAT:QUES:INST:ISUM2? / 128
Errors	312,"Cannot execute when the channels are coupled"
Related Commands	INSTrument:COUPle:TRACking / [SOURce[<n>]]:VOLTage:SENSe[:SOURce] / STATus:QUEStionable:INSTrument[:EVENt]?

### SIMUlator:TEMPerature
Syntax	SIMUlator:TEMPerature {<temperature>}[, {<sensor>}] / SIMUlator:TEMPerature?[ {<sensor>}]
Description	Use this command to set temperature in degrees Celsius (oC) that will “sense” temperature sensor.
Parameters	Name	Type	Range	Default
	<temperature>	Numeric	0 – 100	–
	<sensor>	Discrete	AUX|CH1|CH2	AUX
Return	The query command returns the set temperature value.
Usage example	SIMU:TEMP 45, CH2 / MEAS:TEMP? CH2 / 45.00
Related Commands	MEASure[:SCALar]:TEMPerature[:THERmistor][:DC]

### SIMUlator:VOLTage:PROGram:EXTernal
Syntax	SIMUlator:VOLTage:PROGram:EXTernal {<voltage>} / SIMUlator:VOLTage:PROGram:EXTernal?
Description	Use this command to set voltage that will be used for output voltage programming when channel is in external / remote programming mode (see [SOURce[<n>]]:VOLTage:PROGram[:SOURce]). For full range apply 2.5 V and if higher value is entered channel’s OVP will trip.
Parameters	Name	Type	Range	Default
	<voltage>	Numeric	Positive value	0.00
Return	The query command returns the external output voltage programming value.
Usage example	VOLT:PROG EXT / SIMU:VOLT:PROG:EXT 1.25 / MEAS? / 20.00
Errors	312,"Cannot execute when the channels are coupled"
Related Commands	INSTrument:COUPle:TRACking / [SOURce[<n>]]:VOLTage:PROGram[:SOURce] / [SOURce[<n>]]:VOLTage:PROTection:TRIPped?