# Software simulator
The PSU firmware can be also compiled and executed as a Windows, Linux or OS X application. The software simulator is a terminal application that can respond to any currently supported SCPI command described in this document. SCPI commands could be entered directly in the simulator’s terminal window (Fig. 1) or remotely by using the e.g. a Telnet client (Fig. 2).

Fig. 1: Simulator welcome screen

Fig. 2: Remote connection using a telnet client
The simulator also has a GUI part when started open a separate window with the picture of the PSU front panel.

Fig. 3: Simulator GUI front panel
The GUI simulator front panel currently displays only changes in LED indicators and indicates if load is applied on the output terminals or not. For example if 8.2 Ohm load is connected to the channel 1 and cause that channel enters CC mode the GUI front panel will indicate that in the following way:

Fig. 4: Simulator GUI with connected load on the channel 1
## SIMUlator
The SIMUlator subsystem represent a set of unclassified SCPI commands that can be used to manage external parameters and events such as load impedance, connection and disconnection of the load, sensor temperature or the PSU control circuit power supply state. Thanks to them e.g. simulation of the measuring and protection commands that depends of external events become more meaningful.
For example MEASure:CURRent? without connected load will always returns zero, or activation of the VOLTage:PROTection:STATe will automatically trip the OVP since channel cannot starts in CC mode of operation when output is switched on, etc.

SCPI command	Description
SIMUlator
:EXIT	Closes simulator
:GUI	Starts simulator’s GUI
:LOAD {<value>}	Sets value of the virtual load
:STATe {<bool>}	“Connects” virtual load to the channel output
:PWRGood {<bool>}	Sets the PWRGOOD signal state
:TEMP {<value>}	Sets the temperature sensor value

### SIMUlator:EXIT
Syntax	SIMUlator:EXIT
Description	This command close all Software simulators windows (terminal and GUI if started).
Return	None
Usage example	SIMU:EXIT
Errors
Related Commands

### SIMUlator:GUI
Syntax	SIMUlator:GUI
Description	Use this command to start the GUI simulator in the new window. See Fig. 3
Return	None
Usage example	SIMU:GUI
Errors
Related Commands

### SIMUlator:LOAD
Syntax	SIMUlator:LOAD {<value>} / SIMUlator:LOAD?
Description	This command is used to define impedance of the virtual load that is connected to the channel output. Units are in ohms. With load connected it is possible to simulate e.g. CC mode of operation, current and power measurement, OCP and OPP functionality, etc. / The simulator currently cannot emulate the “UR” mode of operation (see the OUTPut:MODE? command).
Parameters	Name	Type	Range	Default
	<value>	Numeric	0 – 9999999|INFinite	–
Return	The query command returns the programmed load value.
Usage example	SIMU:LOAD 10
Errors
Related Commands	OUTPut:MODE?

### SIMUlator:LOAD:STATe
Syntax	SIMUlator:LOAD:STATe {<bool>} / SIMUlator:LOAD?
Description	This command is used to “connect” or “disconnect” the virtual load to the channel output. If the GUI simulator is started (the SIMUlator:GUI command) load symbol with selected value in Ohms will be displayed (See Fig. 4)
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	–
Return	The query command returns the load state.
Usage example	SIMU:LOAD:STAT? / 0 / MEAS:CURR? / 0.00 / SIMU:LOAD:STAT ON / MEAS:CURR? / 1.50
Errors
Related Commands	OUTPut:MODE? / SIMUlator:GUI / SIMUlator:LOAD

### SIMUlator:PWRGood
Syntax	SIMUlator:PWRGood {<bool>} / SIMUlator:PWRGood?
Description	This command can be used to simulate detection of an internal power supply failure. When PWRGOOD signal is changed from 1 to 0 the PSU is going to the Stand-by mode (equal to the command SYSTem:POW OFF). The PSU mode cannot be changed until PWRGOOD is not changed to 1.
Parameters	Name	Type	Range	Default
	<bool>	Discrete	ON|OFF|0|1	ON
Return	The query command returns the PWRGOOD signal state.
Usage example	SYST:POW? / 1 / SIMU:PWRG 0 / SYST:POW? / 0
Errors
Related Commands	SYSTem:POWer

### SIMUlator:TEMPerature
Syntax	SIMUlator:TEMPerature {<value>} / SIMUlator:TEMPerature?
Description	Use this command to set temperature in degrees Celsius (oC) that will “sense” temperature sensor.
Parameters	Name	Type	Range	Default
	<value>	Numeric	0 – 100	–
Return	The query command returns the set temperature value.
Usage example	SIMU:TEMP 45 / MEAS:TEMP? / 45.00
Errors
Related Commands